CentOS8 UHD and GnuRadio Install

For this installation, as with the others, a Jenkinsfile automatically builds the content within the associated Dockerfile. One Dockerfile is used to build both UHD and GnuRadio in succession.

Since Python 2 support is ending as of January 2021, Python 3 was used for this build. To ensure that Python 3 can be used during the build, the cmake option -DENABLE_PYTHON3=ON must be included. The dependencies listed for the UHD build were included in order to enable the LibUHD, LibUHD - C API, LibUHD - Python API, Examples, Utils, CrimsontTNG, USRP2, MPMD, Manual, and Man Pages components. Enabled components can be verified through the output logs for each build. The PowerTools and epel-release repositories must be enabled to allow for all of these dependencies to be built. Several Python components were installed using Pythons’s pip3 installer.

For the GnuRadio portion of the Dockerfile, the build dependencies were modified from those given from the official GnuRadio wiki for Ubuntu builds to accommodate a source build on CeentOS8. The only GnuRadio component which cannot be built in this install is zeromq.